# Acoustical Baffle Specification for SR-200 PVC Baffle

# SECTION 09800 – ACOUSTICAL CEILING BAFFLES

# PART 1 – GENERAL

1.1	SUMMARY

- This section includes the following:

- Acoustical Ceiling Baffles.

  - SUBMITTALS

- Shop Drawings: Show fabrication and installation details for ceiling baffles, including plans, elevations, sections, details and attachment to other work.

- Submittals:  Furnish 8 1/2” x 11” samples, showing manufacture full range of colors, texture and patterns available for each type of acoustical baffle specified.

- Product Test Report: From a qualified testing agency indicating ceiling baffles comply with requirements.

- Qualification Data: For firms specified in “Quality Assurance” Article to demonstrate their capabilities and experience.

- Product Certificates: Signed by manufacturer certifying that the products furnished comply with requirements.

  - QUALITY ASSURANCE

- Manufacturer Qualification: Manufacture shall have a minimum of 5 years experience in production of specified products and shall furnish supporting documentation showing completed jobs of approximately the same size and scope.

- Fire Test Reports: Provide ceiling baffles with the following surface- burning characteristics as per ASTM E-84.

- Acoustical Test Report: Provide acoustical test report from a qualified testing agency indicating ceiling baffles meets 9.00 sabines/baffle per C423-90a.

  - DELIVERY, STORAGE, AND HANDLING

- Protect Ceiling Baffles from excessive moisture when shipping, storing, and handling.  Deliver in unopened skids and store in a dry place with adequate air circulation.  Do not deliver material until all wet-work has been completed.

# PART 2 – PRODUCTS

  - CEILING BAFFLES, GENERAL

- Ceiling baffles shall be 2” thick – 2.0 lb. per cubic foot density fiberglass.   Manufacturers standard baffle construction, sewn edges, baffle manufactures standard full line of PVC facing.

- Products

- Model # OELEX SR-200 PVC

Sound Seal

Agawam, MA.  USA

Distributed by Oeler Industries, Inc.

Ph. (877) 406-6473

Fax (412) 884-3300

- Facing Material:  Polyvinyl Chloride

- Baffle Thickness: nominal 2” thick

- Noise Reduction: 9.00 sabins/baffle

- Baffle Width: 48 inches

- Baffle Length: As indicated, up to 8 feet long. (standard 2’x4’)

  - CONSTRUCTION

- The acoustical ceiling baffle product shall be supplied in 48” wide baffles with lengths as indicated.  All edges will be stitch bound with grommets for mounting.

  - MOUNTING

A.	Manufactures standard accessories for securely mounting baffles, of type and size indicated and complying with the following requirements:

- Grommets shall be installed to facilitate mounting on either the short of long edge of the baffle, as indicated on the drawing.

2.4	ACOUSTICAL PERFORMANCE

# Sound Absorption: Per ASTM C423-90a

Sabins/Baffle  per Octave Band Center Frequency (Hz)

125	250	500	1000	2000	4000

1.37	4.86	9.21	13.55	8.39	4.7

2.5	FLAMMIBILITY RATING

- Polyvinyl Chloride facing material shall have a Class A Flammability rating per ASTM E-84:  Substrate/core shall have a Class A Flammability rating per ASTM E-84.

# PART 3 – EXECUTION

  - INSTALLATION

- Install Ceiling baffles in locations indicated, top edges level and in alignment with other baffles.   Comply with manufactures written instructions for installation of baffles using type of mounting accessories indicated or, if not indicated, as recommended by manufacture.

  - CLEANING

- After completion of installation of baffles, remove dust and other foreign material according to manufactures written instructions.

- Remove surplus material, rubbish, and debris resulting from baffle installation, on completion of the work, and leave areas of installation in a neat and clean condition.