WoodTrends Acoustical Wood Ceiling System

ELITE Specification

SECTION 09570 – WOOD CEILING / WALLS

PART 1 – GENERAL

1.00 GENERAL

A. WoodTrends Acoustical Wood Ceiling Systems covered by this specification

shall be the products of Sound Seal, 50 H.P. Almgren Drive, Agawam, MA

01001; Phone (800) 569-1294 (413) 789-1770; Fax (413) 789-4444

1.01 SCOPE

A. Sound Seal shall furnish all WoodTrends acoustical wood panel assemblies

necessary to complete installation by contractor in accordance with plans and

specification.

1.02 RELATED WORK BY OTHERS

A. Substrate walls systems and structure and miscellaneous attachment devices

other than those specified herein, are not included.

1.03 QUALITY ASSURANCE

A. Installer Qualification: The installer shall be a firm with a minimum of two (2)

years of successful experience in installation of products with similar

requirements.

B. Fire Performance Characteristics: WoodTrends acoustical wood panels should

be constructed using fire retardant components meeting or exceeding the

requirements of the ASTM E-84 Class (A, B, C )

1. Flame Spread: (25 or less, 26 to 75, 76-200)

2. Smoke Developed: 450 or less

C. Noise Reduction Coefficient: The WoodTrends Elite panels will have a

minimum NRC value of ____, with a (perforation, slot) pattern measuring ____,

when tested in accordance with ASTM C-423.

1.04 PROJECT CONDITIONS

Installation shall be done only when the temperature and humidity closely

approximate the interior conditions that will exist when the building is occupied.

The heating and cooling systems shall be operating before, during, and after

installation, with the humidity of the interior spaces maintained between min.

35% - max. 55%.

Prior to installation panels shall be allowed to stabilize on site 72 hours prior to

installation, the site must be free of wet and dusty trades and the climate

conditions stabilize to normal operational levels.

1.05 SUBMITTALS

A. Submit shop drawings prepared by the manufacturer showing all necessary

details and dimension requirements which will subsequently be field verified

and revised as required by the Architect.

B. Samples: Submit (3sets) 8” x 11” sample panels of each type of product and

finish as specified. Product shall be original production in veneer finish

specified for final use.

C. Certification: Submit to the owner a certificate of compliance to specified

acoustical and fire performance criteria signed by an officer of the panel

manufacturer and attach independent laboratory test results for each product

used, showing that the products supplied as components meet or exceed the

specified requirements.

D. Single Source: All custom acoustical wall and ceiling panels shall be purchased

from a single manufacturer.

1.06 DELIVERY, STORAGE, AND HANDLING

A. Panel assemblies shall be delivered to the project site in original, unopened

packages.

B. Prior to panel installation the site must be free of all wet and dusty trades and the

climatic conditions stabilized to normal operational levels.

C. The panels shall be stored in a fully enclosed space. For a minimum of seventytwo

(72) hours immediately prior to installation, store the panels in the room in

which they will be installed. The temperature and humidity of the room shall

closely approximate those conditions that will exist when the building is

occupied. Store the panels off the floor.

D. Care in handling MUST be exercised to avoid damage.

1.07 WARRANTIES

A. Manufacturer: All materials supplied by the manufacturer shall be guaranteed

against manufacturing defects for one year.

B. Contractor: All work shall be guaranteed for one year from final acceptance of

completed work.

PART 2 – PRODUCTS

2.01 WOODTRENDS ACOUSTIC PANELS

A. Furnish and deliver prefabricated ELITE panels as described in this section for

installation in areas as shown on drawings meeting or exceeding the following

requirements:

Description: WoodTrends ELITE panels, as manufactured by:

Sound Seal Tel: (800) 569-1294

P.O Box 545 Tel: (413) 789-1770

50 H.P Almgren Dr. Fax: (413) 789-4444

Agawam, MA 01001 E-mail: dgilbert@soundseal.com

2.02 PANELS

A. Substrate of fire-retardant 17 mm thick MDF with blind veneer backer

B. 0.6 mm thick real wood veneer face

C. Edge detail

a) Two edges to have 5/16” rabbet

b) One edge to have 1/8” rabbet with 5/16” deep kerf.

c) One edge to have 1/8” rabbet with 5/8” deep kerf and (2) compression

springs allowing automatic alignment of panels on grid.

d) All edges finished with melamine edge banding in matching color.

D. Acoustics

a) Achieved by means of (round perforation measuring _____), or (elongated

slot measuring _____)

b) Acoustic textile adhered to back of panel

2.03 PANEL FINISHES

A. Veneers to be:

a) First Quality select veneer from manufacturer’s standard selection

of 24 real wood species.

b) Additional 40 species available with special veneers staining and

lacquering to match architects samples.

B. Lacquer

a) Two coats UV- polyacrylate

2.04 SUPPORT SYSTEMS

A. (24” x 24”, 24” x 48”, 12” x 72”) ELITE ceiling panels shall be installed by

means of compression spring on intermediate duty 15/16” T-grid. The panels are

to be supplied with compression spring factory supplied.

2.05 ACOUSTICAL PERFORMANCE

Sound Absorption: Per ASTM C – 423

Sound Absorption Coefficient per Octave Band Center Frequency (Hz)

125 250 500 1000 2000 4000 NRC

See Acoustic Test Data page for selections

PART 3 – EXECUTION

3.01 PREPARTION

A. Layout: If required, prior to manufacture, field dimensions shall be taken to

determine panels sizes. The contractor shall measure applicable areas prior to

installation to confirm application and location of panels supports, in accordance

with installation instructions.

B. Coordination: The contractor shall coordinate with other trades the location of

devices which will penetrate the panels of interfere with the installation.

Recessed or surface devices located within the panels are to be located and out

in the field.

3.02 INSTALLATION

A. General: Install materials in accordance with manufacturer’s printed instructions

and approved shop drawings. The installation shall comply with applicable

regulations and industry standards.

B. Provide shimming and adjustments as required to maintain consistent alignment

of joints and of finished panel faces.

3.03 ADJUSTMENT, CLEANING, AND REPAIR

A. The contractor shall make final adjustments to level or contours.

B. Upon completion of installation, all ELITE panels shall be cleaned free of dirt,

dust, grease, oils, and fingerprints. Wood surfaces shall be wiped with furniture

polish to enhance the surface finish.

C. All work, which cannot be successfully cleaned or repaired, shall be removed

and replaced.

3.04 INSPECTION

A. Upon completion of installation, the owner’s representative shall inspect all

finished surfaces to ensure that work has been performed in a manner

satisfactory to the owner. Any deficiencies in the installed panels shall be

corrected by the contractor at no additional cost to the owner, or to the

manufacturer.