B-20 NR 2psi Mass Loaded Vinyl Noise Barrier

Part 1-GENERAL

## Summary

### A.	This section includes the following:

#### Non-reinforced Noise Barriers

  - Related Sections

  - Quality Assurance

- Manufacturer Qualification: Manufacturer shall have a minimum of 5 years experience in production of specified products.

- Acoustical

  - Non-reinforced Noise Barrier should have a STC value of at least 31

  - Submittals

- Samples: Furnish 12” x 12” samples.

- Technical data sheets reflecting material thickness, material weight, and Acoustical data.

1.5 Delivery, storage, and handling

- Store in a dry place with adequate air circulation.  Store materials where they will be free from accidental damage.

Part 2-PRODUCTS

## Non-reinforced Noise Barriers, General

- Non-reinforced Noise Barrier shall be a 2 lb psf mass loaded vinyl noise barrier

  - Products

    - Model # B-20 NR

Sound Seal

Agawam, MA, USA

wwwsoundseal.com

Ph: 800-569-1294   Fax: 413-789-2248

As Distributed By:

Oeler Industries, Inc.

Pittsburgh, PA, USA

Ph: 877-406-6473

  - Sound Transmission class: 31

  - Standard Width: 54 inches

  - Length: As indicated, up to 30 feet long

  - Acoustical Performance:

Sound Transmission Loss: Per ASTM E 90

Octave Band Center Frequency (Hz)

125	250	500	1000	2000	4000	STC

16	22	26	32	35	40	31

Part 3-EXECUTION

3.1 Installation

A.  Install non-reinforced noise barrier in locations indicated.  Comply with manufacturers written instructions for installation by using type of mounting accessories indicated or, if not indicated, as recommended by the manufacturer.

3.2 Cleaning

- After completion of installation remove dust and other foreign material according to manufacturers written instructions.

- Remove surplus material, rubbish, and debris resulting from acoustical pipe and duct lagging installation, on completion of work, and leave areas of installation in a neat and clean condition.